## Slide 1
CRITICAL EVALUATION
What this model cannot
currently be trusted to tell you
An assessment of CenGeometry's limitations, ranked by severity
Caveat on this review: it was written by the same process that built the tool. Self-assessment is weaker than independent review — an outside critic should repeat it.

## Slide 2
A FAIR STARTING POINT
First, what it genuinely achieves
Traceable calibration
Every dimension but one is derived from a schematic by a re-runnable script. That is better practice than most models of this kind.
Real structural findings
Measurement revealed the shared protofilament lattice and the bent A-C linker. Neither was assumed.
An independent number that matches
Wild-type diameter of 255 nm against ~250 nm measured. Diameter was never fitted.
Honest internal documentation
Failed analyses are parked with their blockers recorded rather than quietly dropped.
The problems below are real, but they are problems of interpretation and calibration — not of workmanship.

## Slide 3
FUNDAMENTAL · THE CRUX
The headline validation is largely circular
The claim: “the measured wild-type value sits at a strain minimum for five parameters independently.”
The problem: the model's energy is the sum of bond gaps and deviations from rest angles — and those rest angles were themselves measured from the wild-type geometry.
Why that makes the minimum near-automatic
1
At the measured configuration, every angle deviation is zero by definition.
The energy is a sum of squares, so zero deviation with near-zero closure gap is its global minimum. Any departure can only raise it.
2
So “wild type is optimal” restates how the objective was defined.
It is not an independent prediction. A model built this way would place a minimum at whatever geometry it was calibrated on.
What survives: two things are genuinely non-trivial. That a geometry measured from TWO units closes into a NINE-fold ring at all (to 0.022 nm) — though one parameter was fitted to help. And that the resulting diameter, 255 nm, matches the ~250 nm measured independently. The diameter agreement is the real validation; the strain minima are largely bookkeeping.

## Slide 4
FUNDAMENTAL
Everything rests on one hand-drawn schematic
Sample size of one
All dimensions come from a single drawing of two units. There is no biological replicate, no error bar on any input, and no way to propagate uncertainty to the outputs.
The source contradicts itself
The schematic's two triplets sit 41.4° apart while its two spokes sit exactly 40° apart. A 9-fold structure cannot be both. The model resolves this by enforcing exact symmetry and absorbing the discrepancy elsewhere.
Reading noise sets the floor
Protofilament positions were recovered from text-label anchors, carrying ~2° (~0.4 nm) of error. Numbers are reported to 0.01 nm — three orders of magnitude finer than the calibration supports.
One input is fitted, not measured
The SAS-6 head-head spacing cannot be read off the drawing and is tuned so wild type closes. That is the same parameter the closure validation then relies on.

## Slide 5
FUNDAMENTAL
It is one flat slice of a helical object
The centriole twists along its length. A single cross-section cannot represent that, and the consequence is not hypothetical — it already blocked a real investigation.
Worked example: the blooming question
A published iris-like motion is described as arising from A-C linker twist in the LONGITUDINAL direction. The model was run and returned a confident negative — no in-plane iris mode exists. That answer is irrelevant to the claim, because the claim is about a motion the model cannot represent. The investigation was parked for exactly this reason.
The general risk
A 2D model still returns a confident-looking number when asked a 3D question. Nothing in the output flags that the question was out of scope. Any result about twist, axial gradients, procentriole elongation or stacked cartwheel layers should be treated as unanswerable rather than answered.
Out-of-plane tilt also gives real interfaces accommodation the model lacks — so strain is probably overestimated.

## Slide 6
SECOND TIER
Fixable: the numbers behind the verdicts
Joint thresholds are invented
OK / HARD / SEVERE limits were reasoned, not measured. Tested: scaling all bands 0.5×–2× leaves the qualitative conclusion intact, but flips the spoke's label between OK and HARD. So the ranking is robust; the labels are not.
Bond strengths are ordinal
Six bonds carry values from 1.00 to 0.25 encoding only a rank order. The model then reports a specific “closest to rupture” bond and a numeric load. That precision is not supported by the input — only the ordering is.
No absolute energy scale
Without bond energies in kT, nothing converts to a predicted fluctuation amplitude comparable with data. This is exactly what made the soft-mode analysis uninterpretable and led to it being abandoned.
Strand thickness is assumed
Clearance and the steric term count a 1 nm strand half-width that was never measured — deliberately not fitted, since tuning it to match a mutant diameter would make the result restate the input. Any clearance within a few tenths of zero is therefore marginal. The companion reachability test needs no such number and is the firmer of the two.
A band_sensitivity() helper exists and should be run on any conclusion before it is reported.

## Slide 7
SECOND TIER
Fixable: the solver is not dependable at the edges
Timings are no longer the problem — the chain solver and a vectorised steric test brought every configuration under three seconds. What remains is that robustness had to be added, not designed in:
Chart: Wall-clock per configuration (chain solver)
| wild type | 8 cw / 9 mt | n_pf = 9 | n_pf = 18 | spoke 28 nm
Solve time (s) | 0.44 | 1.28 | 1.7 | 2.86 | 0.86
A crash reachable from the interface
A singlet centriole at a shifted register made the trust-region step's dense factorisation fail outright. It now retries iteratively, but it was reachable by two clicks and nothing had caught it.
An expectation was wrong, then the correction went stale too
Clashes were first predicted at extreme protofilament counts, then 'tested: zero clashes 9 through 18'. Under the current solver n_pf = 9 and 18 both clash again. The original expectation was right; the correction had simply been measured on a superseded architecture.
Accuracy is still traded for responsiveness
Solver effort is capped in the interface so it cannot stall, so extreme configurations return lower-confidence answers by design.
The middle point is the one to sit with: a stated result survived an architecture change without being re-tested — and so did the correction that replaced it. Numbers in slides decay silently.

## Slide 8
WORKED EXAMPLE
Case study: a result that was wrong for two years' worth of reasons
The register search was used to argue a published-quality conclusion about a measured mutant. Two defects in it were found only when the drawing was questioned — not by any test.
Rest angles were not re-referenced when the register shifted
Contact rest orientations are measured in the tubule's own frame. Sliding a contact by one protofilament rotates the site by 360/13 = 27.7° in that frame, but the rest angle stayed put. Every shifted candidate was charged 27.7° of strain that did not exist — past the 20° HARD limit before anything moved. The ranking was bookkeeping.
Nothing stopped a strand lying inside a microtubule
Penetration was measured but never entered the objective, and the measurement itself discarded 3 nm from both ends of every segment — over half of an 11.6 nm linker arm, including exactly the stretch where a bad register shows. The search's winner reached its site 1.7° above tangential, straight along the tubule wall.
What it cost
The register that reproduced the measured diameter, and the mechanism built on it, sits at or past the edge of what is geometrically reachable. The prediction in the project's own notes had to be withdrawn and rewritten.
Neither defect made anything crash, and neither showed up in any number the tool printed. They surfaced because a picture looked wrong. That is not a reliable detector.

## Slide 9
BEFORE PUBLICATION
What would have to change
Requirement | Why it is blocking | Effort
Validate against data NOT used in calibration | Removes the circularity. Predict a mutant or a species the model has never seen, then measure it. | High
Calibrate joint bands on sub-tomogram variance | Converts invented thresholds into measured ones; makes grades meaningful in absolute terms. | Medium
Propagate input uncertainty to outputs | Every number is currently a point estimate from one noisy drawing. Error bars are needed. | Medium
Put bond strengths on an absolute scale | Required before any force, rupture or fluctuation claim can be quantitative. | High
State the scope boundary in the output | So a 3D question cannot silently receive a 2D answer. | Low
None of these invalidate the tool as a hypothesis generator. They are what stand between it and a quantitative claim.

## Slide 10
What you can and cannot conclude today
SAFE
Relative comparisons — mutant against wild type, one perturbation against another
The ordering of which connection is most loaded
Whether a proposed architecture is geometrically possible at all
Diameter predictions, the one output with independent support
Generating hypotheses worth testing at the bench
NOT SAFE
“Wild type is optimal” as an independent finding — it is largely built in
Absolute strain values, forces, or rupture thresholds
Any claim about twist, axial gradients or assembly over time
Precision beyond about 1 nm and a few degrees
Negative results on questions the 2D geometry cannot represent
Bottom line: a well-built hypothesis generator that has not yet been independently validated. Use it to decide what to measure, not to conclude what is true.